Rev 1
- agSteer is connected to the IMU(BNO055) over the I2C interface.
- IMU data is sent in the autosteer packet to AOG over UDP
- ZED9-FP is connected to the agGnssBridge over the serial port - GGA and VTG messages received from the F9P are echoed on the UDP network.
- agGnssBridge also serves as a soft access point for the mobile WiFi network. (RoverNet)

---
Rev 2
- Due to I2C issues, the IMU(BNO055) is relocated to a new module (agImu) running on the Particle Photon processor. .
- The soft access point function is relocated to a separate module (agPureAp).
- agPureAp, agImu, agRtkRover, and agGnssBridge are all under the cover of a single physical package mounted in the tractor cab.
  The charts that follow describe the basic function of the solution.

---
915MHz LoRa
GNSS Antenna
agRtkRover
receives Rtk
corrections
over LoRa ...
ZF9-P
corrects local
GPS coords ...
and pumps them over I2C to the ZF9-P
and pumps GGA messages over UART to the bridge
agGnssBridge
sends GGA over
the UDP network
TCP/IP
Network
images/block-diagram_1.png

---
agIMU
sends IMU data
to the network
images/block-diagram_2.png

---
agSteer
agDru
Motor Drive
and
current monitor
Steer Interlock
Wheel Angle Sensor
images/block-diagram_3.png
Steer Motor

---
agPureAp
WiFi
Access Point
images/block-diagram_4.png

---
GNSS Antenna
915MHz LoRa
ZF9-P
agRtkBase
manages RTK
survey-in, receives
data from F9-P and
streams data to
Rover
images/block-diagram_5.png

---
Rev 2 (5/23)
- The standalone IMU source (agIMU) is eliminated.
- The GNSS bridge function (agGnssBridge) is replaced by the agBridge unit.
- The agBridge unit is connected to the ZED9-FP over the Serial port.
- The agBridge unit is connected to the IMU(BNO085) over the I2C interface.
- The agBridge unit merges data from the IMU with data from the GGA and VTG (NMEA) messages to create a custom $PANDA message which is sent to AOG via UDP.
  The following datagrams only are passed over the UDP network:
  - $PANDA messages from agBridge
  - Hello and Scan messages from AOG
  - Hello and Scan responses from agSteer and agBridge(?)
  - Command packets from AOG → agSteer
  - The autosteer packet from agSteer → AOG

---
915MHz LoRa
GNSS Antenna
agRtcm
receives RTCM
corrections
over LoRa ...
ZF9-P
corrects local
GPS coords ...
and pumps them over I2C to the ZF9-P
and pumps GGA,VTG messages over UART to the bridge
IMU (BNO085)
agBridge
generates and
sends $PANDA over
the UDP network
images/block-diagram_1.png